Using JTAG Debugging on Raspberry Pi's.
# Introduction
It all started with the work of David Welch dwelch@dwelch.com (https://github.com/dwelch67). But a lot of details were missing for me, because I wanted to use the Blinker program to test debugging a Raspberry via a JTAG connection on different Pi versions. I used Openocd in combination with versions of FTDI serial interfaces as the JTAG interface. The baremetal program to blink a LED on different versions of the Raspberry Pi was used a the starting point. All tested in July 2025.
It turned out that it was not that simple as I hoped it would be. A lot of details needed to be in place before debugging via JTAG a Raspberry Pi was possible. Each version Pi needs a slightly different setup.
# Blinker Program
This README file is common for all Blinker sub projects:
- For the Raspberri Pi 4B: 32bit and 64bit version
  - 4B\BareMetal32bit_Blinker
  - 4B\BareMetal64bit_Blinker
- For the Raspberri Pi Zero2W: 32bit and 64bit version
  - Zero2W\BareMetal32bit_Blinker
  - Zero2W\BareMetal64bit_Blinker
- For the Raspberri Pi ZeroW1.1: 32bit version
  - ZeroW1.1\BareMetal32bit_Blinker
It describes the way a Windows system needs to be setup in order to be able to compile and run the Bare metal Blinker program. In each sub project a README file is included with specific details for that project.

The makefile used in each sub project uses the common makefile found in the root directory.
Open powershell and run 'make clean' and 'make' from within each project dir. Then copy all files from the SD_card directory to the root directory of a SD card.

The confix.txt file configures Raspi's for using JTAG pins for debugging.

For the 32 bit version of the Raspberry Pi 4B version, the starting address in src/start.s needs to be at address 0x8000, whereby the 64bit version needs a starting address at 0x80000. The config.txt are different in the way that the 32 bit version has 'arm_64bit=0' included and 'kernel=kernel.img', whereby the 64bit version has 'arm_64bit=1' included and 'kernel=kernel8.img' (if you like you can omit 'kernel=kernel8.img', since this is default).
# JTAG
In the 'openocd' directory you will find the .cfg files for the different FDTI adapters used. In these .cfg files the connections which need to to be made are explained. At least 'TCK', 'TDI', 'TDO', 'TMS' and 'TRST' need to be wired between the FTDI module and the Raspberry Pi. The 'SRST' and 'RTCK' signals are optional (SRST=System Reset, RTCK=Return clock). The 'TRST' resets the JTAG Debug adapter of the Raspberry, whereby the Raspberry itself keeps working. The System Reset, resets the whole Raspberry and by that restarting the CPU and peripherals.
I used 5k6 resistors to pull up or pull down the different signals. 'TCK' needs to be pulled down, the rest pulled up.

I started not using these pull up/down resistors, but after checking with an oscilloscope and/or Pulseview (https://github.com/sigrokproject/pulseview) I noticed that sometimes the voltage levels did not meet the minimum required levels, therefore I soldered these resistors fixed to the FTDI adapters. The SRST can not be found on the P1 connector of the Raspberry but needs to be connected via a 10k resistor to the RUN connection on the Raspberry Pi board (sometimes requires soldering). The RTCK is shown here, but I was not able to get it to work (but is not needed anyway).
# FTDI Adapters
I have used 3 different types of adapters 1-channel (FT232H), 2-channel (FT2232H) and 4-channel (FT4232H). If using the FT232H and you want to use the Serial port of a Raspberry at the same tiem you need to attach a scond adapter. Using the FT2232H makes it possible to connect the JTAG to the first channel and the Serial interface to the second channel. The 4 channel has two ports which can be used as JTAG interface (port o and port 1) whereby the other two (port 2 and 3) can be used as serial interface. The configuration used per type can be found in the 'openocd' directory.
## Drivers
The JTAG interface when used in combination with Openocd requires WinUSB driver. WinUSB driver can be installed using Zadig (https://zadig.akeo.ie/). When reconnecting the adapter (or started my computer again) I needed to reinstall the WinUSB driver again. Also starting OpenOCD with debug option (openocd -d3) and if the debug output gives “Error: 157 1234 mpsse.c:180 open_matching_device(): libusb_open() failed with LIBUSB_ERROR_NOT_SUPPORTED” you know the driver is wrong.
For the Serial port used as a COM port the FTDI driver (https://ftdichip.com/drivers/vcp-drivers/) is needed.
# OpenOCD
I have chosen to compile the source code (https://github.com/openocd-org/openocd) to be sure I had all the options I needed available. See openocd/building_openocd_32bit.txt and openocd/building_openocd_64bit.txt for the 32bit or 64bit version for the way I did it. Since I'm using the Cortex-Debug expansion in Visual Studio Code I had to make some changes to the settings in 'openocd.cfg' (can be found in each project dir). Cortex-Debug uses other ports as standard than OpenOCD does (gdb_port 50000, tcl_port 50001 and telnet_port 50002).
# SD_Card
Special care is needed when using the different Raspberry's. Each Raspberry needs different files and setup. Use the ones supplied in each SD_card subdirectory of the specific project file. The new .img file will be automatically copied to the SD_card directory after (re)compiling.